## Slide 1: ANALYZE 04
Break material into its constituent parts and determine how the parts relate to one another and/or to an overall structure or purpose.

## Slide 2: Examples 01
In this question, student should know the graph of different types of filters. According to the given specification student have to draw the graph and then analyze the type of filter based on the graph.
Determine type of filter based on following specification Ap=3dB,
ωp = 0.5π, As=15dB, ωs=0.75π
a) HPF b) LPF c)Bandpass d)Bandstop

## Slide 3: Examples 02
In this question student should know the formula of order for both types of filter. They have to apply the formula and calculate the order and conclude
Butterworth filter has greater order.
Second conclusion can be drawn after calculating the poles.
Plotting the poles on z plane they will come to know that the Poles of a Butterworth filter lie only on a circle, while that of the Chebyshev filter lie on an ellipse.
A digital LPF is to he designed for following specifications- Passband ripple(Ap) <1db, Stopband ripple (As) >=40db, Passband edge(Fp) = 4Khz , Stopband edge(Fs)=6Khz, Sampling rate(Fsamp) = 24Khz . Compare the above parameters for Butterworth and Chebyshev filters and conclude the difference.

## Slide 4: EVALUATE 05
make judgments based on criteria and standards

## Slide 5: Examples 01
In this question, student should know the difference between filters and which differentiating point they can use to solve this question. For this question they have to plot poles on z plane then analyze the graph and evaluate that the given filter is Butterworth filter because poles of a Butterworth filter lie only on a circle.
Determine what type of IIR filter that will pass all radian frequencies greater than 200 rad/sec with no more that 2db attenuation and have a stop band attenuation of greater than 20db for all Ω less than 200 rad/sec.
a)Butterworth Filter b) Chebyshev Filter c) Elliptic Filter
d)None of these

## Slide 6: Examples 02
In this question, student should know the what is mean by stability in this topic and how to evaluate that system is stable or not they have to calculate poles .
Determine pole and stability of Chebyshev filter with following characteristics: • Acceptance pass band ripple of 2db • Cut-off radian frequency of 1rad/sec • Stop band attenuation of 20db or greater beyond 1.3rad/sec
a) 0.25 -j0.4, Stable b) -0.25 - j0.4, Stable c) -0.25 - j0.4, Unstable
d) 0.25 -j0.4, Unstable

## Slide 7: CREATE 06
put elements together to form a new coherent or functional whole; reorganize elements into a new pattern or structure

## Slide 8: Examples 01
In this question, student should know the formula of order and then they have to recreate the formula in terms of KP and KS.
Propose the order N of the low pass Butterworth filter in terms of KP and KS? b) c)

## Slide 9: Examples 02
In this question, student have to design filter based on all the knowledge and understanding of filter and using steps of design.
Design the digital Butterworth high pass filter for the following specification.
Ap= 3 dB, As= 15 dB, ws=0.5π, wp=0.75π